## Slide 1: Open-Source Industrial Control
Turning 2,800 Tons of Metal with Python and Flask

## Slide 2: Jacob Lapenna
Electrical Engineer at the U.S. Bureau of Reclamation
I design and build cyber-physical systems
Email (burner)
LinkedIn

## Slide 3: Rotating Machines

## Slide 4: Rotating Machines
Notes: Humans for scale. The turning part of this machine weighs 2,800 tons (2,540,117 kg). The drive shaft is the size of a Redwood tree. This machine has been turned with the methods described in this presentation.

## Slide 5: Rotating Machines
The rest is just scale and optimization
N
N
N
N
N
N
S
S
S
S
S
S
Notes: Rotor = the turning magnets
Stator = the stationary winding
Pole = magnetic pole, commonly referred to as north or south poles of a magnet
The rotor turns and moves magnets past the coils formed by the stator winding. The changing magnetic field induces voltage and current flows to the electric grid.

## Slide 6: Slow-Roll Testing
We need slow, precise turning for:
Bearing alignment
Signal mapping

## Slide 7: Slow-Roll Testing
We need slow, precise turning for:
Bearing alignment
Signal mapping

## Slide 8: Slow-Roll Testing
We need slow, precise turning for:
Bearing alignment
Signal mapping

## Slide 9: Slow-Roll Testing
How?

## Slide 10: Slow-Roll Testing
How?

## Slide 11: Slow-Roll Testing
How?

## Slide 12: Slow-Roll Testing
How?

## Slide 13: Industrial Control
Give me a relay contact and I can move the world…
Notes: Archimedes

## Slide 14: DC Stepper Motor
Notes: DC = direct current
DC stepper motor = motor that rotates continuously from a continuous series of steps
Electromagnet = magnet formed by sending current through a loop of wire looped around an iron core

## Slide 15: DC Stepper Motor

## Slide 16: DC Stepper Motor

## Slide 17: DC Stepper Motor
Notes: Phase = one circuit of a three circuit (3-phase) system. Our electrical grid runs on 3-phase power, this lets return current return on another phase rather than requiring neutral wire to run across the country.

## Slide 18: DC Stepper Motor

## Slide 19: DC Stepper Motor
Notes: Three phases
Red phase
Blue phase
Green phase

## Slide 20: DC Stepper Motor
I
N
N
N
N
N
N
N
N
S
S
S
S
S
S
S
S
Notes: Torque = rotational force
Force is parallel to the radius, no torque

## Slide 21: DC Stepper Motor
I
S
S
S
S
S
S
S
S
N
N
N
N
N
N
N
N
Notes: Reverse current, swap magnetic poles, north becomes south and south becomes north
Force is again parallel to the radius, no torque

## Slide 22: DC Stepper Motor
I
S
S
S
S
S
S
S
S
N
N
N
N
N
N
N
N
Notes: Apply current to a different phase not already aligned to produce non-zero torque

## Slide 23: DC Stepper Motor
I
S
S
S
S
S
S
S
S
N
N
N
N
N
N
N
N

## Slide 24: DC Stepper Motor
I
S
S
S
S
S
S
S
S
N
N
N
N
N
N
N
N

## Slide 25: DC Stepper Motor
I
S
S
S
S
S
S
S
S
N
N
N
N
N
N
N
N
Notes: Apply current in the other direction to get torque in the other direction

## Slide 26: Prototype (2020)
Small power supply for rotor
Large power supply for stator
Current reverser
Manual switch controller

## Slide 27: Prototype (2020)
Small power supply for rotor
Large power supply for stator
Current reverser
Manual switch controller
Notes: Power supply

## Slide 28: Prototype (2020)
Small power supply for rotor
Large power supply for stator
Current reverser
Manual switch controller

## Slide 29: Prototype (2020)
Small power supply for rotor
Large power supply for stator
Current reverser
Manual switch controller

## Slide 30: Prototype (2020)
Small power supply for rotor
Large power supply for stator
Current reverser
Manual switch controller

## Slide 31: Prototype (2020)
Small power supply for rotor
Freewheel diode
Large power supply for stator
Current reverser
Manual switch controller
Drawbacks
Specialized & hard to use
Only visual positioning
Not very modular

## Slide 32: Prototype (2020)
Small power supply for rotor
Freewheel diode
Large power supply for stator
Current reverser
Manual switch controller
Drawbacks
Specialized & hard to use
Only visual positioning
Not very modular

## Slide 33: Prototype (2020)
Small power supply for rotor
Freewheel diode
Large power supply for stator
Current reverser
Manual switch controller
Drawbacks
Specialized & hard to use
Only visual positioning
Not very modular

## Slide 34: Python + Raspberry Pi
Notes: Flask
Flask-SocketIO
Scoket.IO
Celery
Redis
I2C
Digilent
Python
Raspberry Pi (CM4 model)

## Slide 35: Browser Application
Why browser-based industrial control?
Plaintext
No installation/Sandboxed
Reduced training
Proven
Creative visualization
Highly interactive
Support
Scalable

## Slide 36: Browser Application
Why browser-based industrial control?
Plaintext
No installation/Sandboxed
Reduced training
Proven
Interactive visualization
Support
Scalable
Notes: Human readable version tracking without procurement of extra proprietary software.

## Slide 37: Browser Application
Why browser-based industrial control?
Plaintext
No installation/Sandboxed
Reduced training
Proven
Interactive visualization
Support
Scalable
Notes: Government furnished equipment, security, etc.

## Slide 38: Browser Application
Why browser-based industrial control?
Plaintext
No user installation
Reduced training
Proven
Interactive visualization
Support
Scalable
Notes: Everyone know how to use a browser. It’s intuitive at this point.

## Slide 39: Browser Application
Why browser-based industrial control?
Plaintext
No installation/Sandboxed
Reduced training
Proven
Interactive visualization
Support
Scalable
Notes: The internet and its underlying technology is incredibly user tested, proven, and well backed.

## Slide 40: Browser Application
Why browser-based industrial control?
Plaintext
No installation/Sandboxed
Reduced training
Proven
Interactive visualization
Support
Scalable

## Slide 41: Browser Application
Why browser-based industrial control?
Plaintext
No installation/Sandboxed
Reduced training
Proven
Interactive visualization
Support
Scalable
Notes: Easier to hire for (vs traditional SCADA). From going to space to automatic cat feeders, Raspberry Pi may be one of the most used and abused pieces of hardware in the world. Also, NASA has even published a “Raspberry Pis for Space Guideline”.

## Slide 42: Browser Application
Why browser-based industrial control?
Plaintext
No installation/Sandboxed
Reduced training
Proven
Interactive visualization
Support
Scalable
Notes: Celery makes task distribution and scaling easy

## Slide 43: Browser Application
Con: not truly real-time (but so what)
Notes: Ladder logic = type of visual programing commonly used in PLCs
PLC = programmable logic controller (the typical device used for industrial control)
Real-time operating system = operating system that makes promises on tasks completed in a certain amount of time.

## Slide 44: Browser Application
Security (air gap)
The Cloud / Internet
Notes: Air gap = network that is not physically or wirelessly connected to larger networks like the internet and “the cloud”.

## Slide 45: Modular Design (Hardware)

## Slide 46: Modular Design (Hardware)
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DISTRIBUTION BOX
STATOR BOX
ROTOR BOX
DISTRIBUTION BOX
DC SUPPLY BOX
STATOR WINDING
ROTOR WINDING
Notes: 480 V power

## Slide 47: Modular Design (Hardware)
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DISTRIBUTION BOX
STATOR BOX
ROTOR BOX
DISTRIBUTION BOX
DC SUPPLY BOX
STATOR WINDING
ROTOR WINDING
Notes: 480 V power

## Slide 48: Modular Design (Hardware)
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DISTRIBUTION BOX
STATOR BOX
ROTOR BOX
DISTRIBUTION BOX
DC SUPPLY BOX
STATOR WINDING
ROTOR WINDING

## Slide 49: Modular Design (Hardware)
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DISTRIBUTION BOX
STATOR BOX
ROTOR BOX
DISTRIBUTION BOX
DC SUPPLY BOX
STATOR WINDING
ROTOR WINDING

## Slide 50: Modular Design (Hardware)
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DISTRIBUTION BOX
STATOR BOX
ROTOR BOX
DISTRIBUTION BOX
DC SUPPLY BOX
STATOR WINDING
ROTOR WINDING

## Slide 51: Modular Design (Hardware)
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DISTRIBUTION BOX
STATOR BOX
ROTOR BOX
DISTRIBUTION BOX
DC SUPPLY BOX
STATOR WINDING
ROTOR WINDING

## Slide 52: Modular Design (Hardware)
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DISTRIBUTION BOX
STATOR BOX
ROTOR BOX
DISTRIBUTION BOX
DC SUPPLY BOX
STATOR WINDING
ROTOR WINDING

## Slide 53: Modular Design (Hardware)
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DISTRIBUTION BOX
STATOR BOX
ROTOR BOX
DISTRIBUTION BOX
DC SUPPLY BOX
STATOR WINDING
ROTOR WINDING
Notes: OPR = once per revolution. A sensor that detects one revolution of the rotor.
Rotary encoder = a sensor that tracks rotational position

## Slide 54: Modular Design (Hardware)
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DISTRIBUTION BOX
STATOR BOX
ROTOR BOX
DISTRIBUTION BOX
DC SUPPLY BOX
STATOR WINDING
ROTOR WINDING

## Slide 55: Modular Design (Hardware)
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DISTRIBUTION BOX
STATOR BOX
ROTOR BOX
DISTRIBUTION BOX
DC SUPPLY BOX
STATOR WINDING
ROTOR WINDING

## Slide 56: Modular Design (Hardware)
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DC SUPPLY BOX
DISTRIBUTION BOX
STATOR BOX
ROTOR BOX
DISTRIBUTION BOX
DC SUPPLY BOX
STATOR WINDING
ROTOR WINDING

## Slide 57: Modular Design (Hardware)
Notes: McMaster Carr and Automation Direct are great to source components from as they provide a CAD drawing for almost all the products they sell.

## Slide 58: Modular Design (Hardware)
Notes: Faceplate = the outer plate that the user sees and interacts with. Must be machines to fits all plugs, connectors, fans, etc in a neat and visually appealling way.

## Slide 59: Modular Design (Hardware)
Notes: Everything is mounted to faceplate for easy maintenance

## Slide 60: Modular Design (Software)
Distributed computing
Rotor Control
Detects event requests
Publishes tasks to message broker
Stator Control
Assigned a message queue
Monitors for tasks in queue
Redis Connection
Notes: Distributed comuting = the same application carrying out computing tasks over distributed hardware

## Slide 61: Modular Design (Software)
Distributed computing
Rotor Control
Detects event requests
Publishes tasks to message broker
Stator Control
Assigned a message queue
Monitors for tasks in queue
Redis Connection

## Slide 62: Modular Design (Software)
Distributed computing
Rotor Control
Detects event requests
Publishes tasks to message broker
Stator Control
Assigned a message queue
Monitors for tasks in queue
Redis Connection

## Slide 63: Modular Design (Software)
Distributed computing
Rotor Control
Detects event requests
Publishes tasks to message broker
Stator Control
Assigned a message queue
Monitors for tasks in queue
Redis Connection
Notes: Message broker = Redis
Message queue

## Slide 64: Modular Design (Software)
Distributed computing
Rotor Control
Detects event requests
Publishes tasks to message broker
Stator Control
Assigned a message queue
Monitors for tasks in queue
Redis Connection

## Slide 65: Modular Design (Software)
Distributed computing
Rotor Control
Detects event requests
Publishes tasks to message broker
Stator Control
Assigned a message queue
Monitors for tasks in queue
Redis Connection

## Slide 66: Modular Design (Software)
Distributed computing
Rotor Control
Detects event requests
Publishes tasks to message broker
Stator Control
Assigned a message queue
Monitors for tasks in queue
Redis Connection

## Slide 67: Modular Design (Software)
Distributed computing
Rotor Control
Stator Control
Air Gap Measurement Control
Partial Discharge Mapping Control
And more…

## Slide 68: Event Example: Forward Rotation

## Slide 69: Event Example: Forward Rotation

## Slide 70: Event Example: Forward Rotation

## Slide 71: Event Example: Forward Rotation

## Slide 72: Event Example: Forward Rotation
rtts/rotor/templates/manual_turn.html
<!DOCTYPE html>
<html>
<head> <title>RTTS Manual Turning</title>
<script src="{{ url_for('static', filename='js/socket.io.min.js') }}"></script>
... </head>
<body> ...
<button id="forward_button">FORWARD</button> ... <script type="module" src="{{ url_for('static', filename='js/manual_turn_main.js') }}">
</script> </body>
</html>
user
rotor
stator

## Slide 73: Event Example: Forward Rotation
rtts/rotor/templates/manual_turn.html
<!DOCTYPE html>
<html>
<head> <title>RTTS Manual Turning</title>
<script src="{{ url_for('static', filename='js/socket.io.min.js') }}"></script>
... </head>
<body> ...
<button id="forward_button">FORWARD</button> ... <script type="module" src="{{ url_for('static', filename='js/manual_turn_main.js') }}">
</script> </body>
</html>
user
rotor
stator

## Slide 74: Event Example: Forward Rotation
rtts/rotor/static/js/manual_turn_main.js
...
forward_button.ontouchstart = function(event) {
current_on(event, this, events.MANUAL_TURNING.DIRECTION.FORWARD, lead);
}
...
function current_on(event, element, direction, lead) {
// button and request light gets styled here...
if (lead !== null) {
socket.emit(
events.MANUAL_TURNING.TURN_ON,
{"direction" : direction, "lead" : lead}
);
}
}
...
user
rotor
stator

## Slide 75: Event Example: Forward Rotation
rtts/rotor/static/js/manual_turn_main.js
...
forward_button.ontouchstart = function(event) {
current_on(event, this, events.MANUAL_TURNING.DIRECTION.FORWARD, lead);
}
...
function current_on(event, element, direction, lead) {
// button and request light gets styled here...
if (lead !== null) {
socket.emit(
events.MANUAL_TURNING.TURN_ON,
{"direction" : direction, "lead" : lead}
);
}
}
...
user
rotor
stator

## Slide 76: Event Example: Forward Rotation

## Slide 77: Event Example: Forward Rotation
rtts/rotor/static/js/manual_turn_main.js
...
forward_button.ontouchstart = function(event) {
current_on(event, this, events.MANUAL_TURNING.DIRECTION.FORWARD, lead);
}
...
function current_on(event, element, direction, lead) {
// button and request light gets styled here...
if (lead !== null) {
socket.emit(
events.MANUAL_TURNING.TURN_ON,
{"direction" : direction, "lead" : lead}
);
}
}
...
user
rotor
stator

## Slide 78: Event Example: Forward Rotation
rtts/rotor/events.py
@socketio.on(event.names.MANUAL_TURNING.TURN_ON)
def request_current_on(requested_state: dict):
lead = requested_state["lead"]
if lead:
current_amps = int(cache_conn.get(CacheKeys.STATOR_CURRENT_LIMIT))
cel.send_task(
"rtts.stator.turn_on",
args=[requested_state["direction"], lead, current_amps]
)
user
rotor
stator

## Slide 79: Event Example: Forward Rotation
rtts/rotor/events.py
@socketio.on(event.names.MANUAL_TURNING.TURN_ON)
def request_current_on(requested_state: dict):
lead = requested_state["lead"]
if lead:
current_amps = int(cache_conn.get(CacheKeys.STATOR_CURRENT_LIMIT))
cel.send_task(
"rtts.stator.turn_on",
args=[requested_state["direction"], lead, current_amps]
)
user
rotor
stator

## Slide 80: Event Example: Forward Rotation
/var/log/celery/celery.log
user
rotor
stator
[2024-04-19 13:32:29,292: INFO/MainProcess] Task rtts.stator.turn_on [<event ID here>] received

## Slide 81: Event Example: Forward Rotation
rtts/stator/tasks.py
@cel.task(name="rtts.stator.turn_on")
def turn_on(direction: str, lead: str):
if direction == event.names.MANUAL_TURNING.DIRECTION.FORWARD:
if lead == event.names.MANUAL_TURNING.LEAD.X:
SCRs.X_FORWARD.fire()
elif lead == event.names.MANUAL_TURNING.LEAD.Y:
SCRs.Y_FORWARD.fire()
elif direction == event.names.MANUAL_TURNING.DIRECTION.REVERSE:
...
on_states = bus.set_current_limits(current_amps)
socketio.emit(event.names.MANUAL_TURNING.CONFIRMED_ON, on_states)
user
rotor
stator

## Slide 82: Event Example: Forward Rotation
rtts/stator/tasks.py
@cel.task(name="rtts.stator.turn_on")
def turn_on(direction: str, lead: str):
if direction == event.names.MANUAL_TURNING.DIRECTION.FORWARD:
if lead == event.names.MANUAL_TURNING.LEAD.X:
SCRs.X_FORWARD.fire()
elif lead == event.names.MANUAL_TURNING.LEAD.Y:
SCRs.Y_FORWARD.fire()
elif direction == event.names.MANUAL_TURNING.DIRECTION.REVERSE:
...
on_states = bus.set_current_limits(current_amps)
socketio.emit(event.names.MANUAL_TURNING.CONFIRMED_ON, on_states)
user
rotor
stator

## Slide 83: Event Example: Forward Rotation
SCR Circuit
user
rotor
stator
GPIO 5
SCR Firing Board
Relay
SCRs

## Slide 84: Event Example: Forward Rotation
SCR Circuit
user
rotor
stator
GPIO 5
SCR Firing Board
Relay
SCRs

## Slide 85: Event Example: Forward Rotation
SCR Circuit
user
rotor
stator
GPIO 5
SCR Firing Board
Relay
SCRs

## Slide 86: Event Example: Forward Rotation
SCR Circuit
user
rotor
stator
Notes: Optical isolation relay

## Slide 87: Event Example: Forward Rotation
SCR Circuit
user
rotor
stator
Notes: 24 VDC through primary side of pulse transformer to a mossfet

## Slide 88: Event Example: Forward Rotation
SCR Circuit
user
rotor
stator
Notes: Mosfet is pulsed to control ground side of primary side of pulse transformer.

## Slide 89: Event Example: Forward Rotation
SCR Circuit
user
rotor
stator
Notes: Pulse is sent to SCR to reduce gat circuit power consumption. High frequency is used so that when anode is biased, the next gate pulse fires the SCR.

## Slide 90: Event Example: Forward Rotation
SCR Circuit
user
rotor
stator
GPIO 5
SCR Firing Board
Relay
SCRs
Notes: GPIO = general purpose input and output
SCR = silicon-controlled rectifier. Four-layer silicon switching to control very high currents with minimal power. It’s like a very high-current transistor (though transistors are 3-layer silicon).

## Slide 91: Event Example: Forward Rotation
SCR Circuit
user
rotor
stator

## Slide 92: Event Example: Forward Rotation
SCR Circuit
user
rotor
stator

## Slide 93: Event Example: Forward Rotation
SCR Circuit
user
rotor
stator

## Slide 94: Event Example: Forward Rotation
SCR Circuit
user
rotor
stator

## Slide 95: Event Example: Forward Rotation
SCR Circuit
user
rotor
stator

## Slide 96: Event Example: Forward Rotation
rtts/stator/tasks.py
@cel.task(name="rtts.stator.turn_on")
def turn_on(direction: str, lead: str):
if direction == event.names.MANUAL_TURNING.DIRECTION.FORWARD:
if lead == event.names.MANUAL_TURNING.LEAD.X:
SCRs.X_FORWARD.fire()
elif lead == event.names.MANUAL_TURNING.LEAD.Y:
SCRs.Y_FORWARD.fire()
elif direction == event.names.MANUAL_TURNING.DIRECTION.REVERSE:
...
on_states = bus.set_current_limits(current_amps)
socketio.emit(event.names.MANUAL_TURNING.CONFIRMED_ON, on_states)
user
rotor
stator

## Slide 97: Event Example: Forward Rotation
rtts/stator/tasks.py
@cel.task(name="rtts.stator.turn_on")
def turn_on(direction: str, lead: str):
if direction == event.names.MANUAL_TURNING.DIRECTION.FORWARD:
if lead == event.names.MANUAL_TURNING.LEAD.X:
SCRs.X_FORWARD.fire()
elif lead == event.names.MANUAL_TURNING.LEAD.Y:
SCRs.Y_FORWARD.fire()
elif direction == event.names.MANUAL_TURNING.DIRECTION.REVERSE:
...
on_states = bus.set_current_limits(current_amps)
socketio.emit(event.names.MANUAL_TURNING.CONFIRMED_ON, on_states)
user
rotor
stator

## Slide 98: Event Example: Forward Rotation
user
rotor
stator
...
socket.on(events.MANUAL_TURNING.CONFIRMED_ON, function(on_states) {
confirm_light.style.backgroundColor = confirm_color;
});
...
rtts/rotor/static/js/manual_turn_main.js

## Slide 99: Event Example: Forward Rotation

## Slide 100: Event Example: Forward Rotation

## Slide 101: Sensing

## Slide 102: Sensing: Once per Revolution (OPR)

## Slide 103: Sensing: Rotary Encoder
Notes: Slip ring = the metal ring that carbon brushes slip against to transfer current to the turning rotor’s electromagnets
Slip ring circumference is unknow. Drive ratio is different for every machine.

## Slide 104: Sensing
MCC 152 DAQ HAT
8 channel digital I/O
Stack up to 8
Python daqhats API
Notes: MCC 152 = measurement computing (now Digilent) product to detect digital signals
DAQ = data acquisition
HAT = Hardware Attached on Top. A device that can plug directly into the Raspberry Pi’s GPIO header and provide some extra functionality. In this case, digital signal acquisition.

## Slide 105: Sensing
MCC 152 DAQ HAT
8 channel digital I/O
Stack up to 8
Python daqhats API

## Slide 106: Sensing
MCC 152 DAQ HAT
8 channel digital I/O
Stack up to 8
Python daqhats API

## Slide 107: Sensing
MCC 152 DAQ HAT
8 channel digital I/O
Stack up to 8
Python daqhats API

## Slide 108: Sensing: Determining Drive Ratio

## Slide 109: Future Work
Automation
Circumference tool
Partial discharge mapping
Air gap measurement
I
S
S
S
S
S
S
S
S
N
N
N
N
N
N
N
N

## Slide 110: Future Work
Automation
Circumference tool
Partial discharge mapping
Air gap measurement
θ
α

## Slide 111: Future Work
Automation
Circumference tool
Partial discharge mapping
Air gap measurement
More Info
Notes: Partial Discharge = ionization of micro-voids in electrical insulation.
When the stator winding is manufactured, micro bubbles can be trapped in the epoxy. These micro-bubbles represent a discrete change in capacitance across the insulation. This can cause them to ionize when expose to high-voltage. This can be detect with a near-field communication (NFC) antenna. Stick an NFC antenna on a rotor pole, turn the rotor while recording antenna signal and position to map activity throughout stator winding. When trended, this can give insight into extent of damage and cost of repair.

## Slide 112: Future Work
Automation
Circumference tool
Partial discharge mapping
Air gap measurement
Notes: Capacitive proximity probes stuck to rotor pole. This measures distance from pole face to stator. It measures close for each stator core tooth and far for each winding slot. Before, a peak detection algorithm was used in post processing to determine air-gap. Now, position of the probe can simply be recorded as the rotor turns and air gap plotted vs position directly.

## Slide 113: Conclusions
IT
OT
Notes: The line between IT (Information Technology) and OT (Operational Technology) is blurring more and more. We need to facilitate edge computing, real time remote monitoring, and ever more complex computing. We want centralized data to train and learn from. All this required more than ladder logic. This require multidisciplinary teams of software and hardware engineers creating innovative automation and using open source in novel ways.

## Slide 114: Questions?
Email (burner)
LinkedIn